NFS
Network File System protocol

---
Network File System
Network File System
originally developed by Sun Microsystems in 1984
allowed a user on a client computer to access files over a computer network
built on the Open Network Computing Remote Procedure Call
NFS is an open standard defined in Request for Comments (RFC)
Sun used version 1 only for in-house experimental purposes
[Speaker Notes: Open Network Computing Remote Procedure Call originally developed by Sun Microsystems in the 1980s as part of their Network File System project, and is sometimes referred to as Sun RPC. RFC - allowing anyone to implement the protocol]

---
NFSv2
NFSv2
1989
public version
UDP support only
2 GB file size limit, due to 32-bit limitations
stateless but with no file locking
[Speaker Notes: https://www.ietf.org/rfc/rfc1094.txt http://docstore.mik.ua/orelly/networking_2ndEd/nfs/ch11_02.htm Used NLM (Network Lock Manager) to handle file locking which is inherently stateful and thus NLM is stateful complex scheme to recover from failures. There are three types of recovery scenarios to consider: Server crash Client crash Network partition All Linux ports for 32-bit CPUs (i.e., all architectures other than Alpha and IA-64) use 32-bit integers for file access and locking, yielding a maximum size of 2^31 - 1 = 2GB]

---
NFSv3
NFSv3
1995
TCP support added
64-bit support added, which lifted the 2GB file size limit
support for asynchronous writes on the server
separate mounted exports
security relied on RPC
[Speaker Notes: https://tools.ietf.org/html/rfc1813 Async. Writes using WRITE / COMMIT http://tools.ietf.org/html/rfc1813#section-3.3.7 http://tools.ietf.org/html/rfc1813#section-3.3.21 Basically it was only unix based security (sys)]

---
NFSv4
NFSv4
2000
exports mounted together under a single directory tree structure
kerberos ACL security added (krb5, krb5i, krb5p)
single protocol for mounting / locking
stateful with built-in support for file locking
[Speaker Notes: https://tools.ietf.org/html/rfc7530 Exports - All of the exports served by the NFSv4 server are exported as a single file system, called the NFSv4 pseudo-file system. On Red Hat Enterprise Linux, the pseudo-file system is identified as a single, real file system, identified at export with the fsid=0 option Single protocol: No need for NLM (Network Lock Manager) No more portmap, rpcbind, rpc.lockd, and rpc.statd Nfs4_setfacl, nfs4_getfacl but GUI requires compilation from http://www.citi.umich.edu/projects/nfsv4/linux/nfs4-acl-tools/ Krb5	Use Kerberos V5 protocol to authenticate users before granting access to the shared filesystem. Krb5i	Use Kerberos V5 authentication with integrity checking (checksums) to verify that the data has not been tampered with. Krb5p	User Kerberos V5 authentication, integrity checksums, and privacy protection (encryption) on the shared filesystem. This provides the most secure filesystem sharing, as all traffic is encrypted. It should be noted that performance might suffer on some systems when using krb5p, depending on the computational intensity of the encryption algorithm and the amount of data being transferred.]

---
NFSv4.1
NFSv4.1
2010
RPCSEC_GSS (to allow more sec. mechanisms)
parallel access (pNFS) for improved performance
Improved compatibility with Microsoft Windows for Access Control Lists
[Speaker Notes: https://tools.ietf.org/html/rfc5661 Open Network Computing (ONC) Remote Procedure Call (RPC) security flavor that allows RPC protocols to access the Generic Security Services Application Programming Interface (GSS-API) pNFS Removes the filer heads bottleneck for reading metadata and the access to the actual data, by creating direct data paths to the storage devices http://www.pnfs.com/ MS ACL compatibility with more ACL attributes]

---
NFSv4.2
NFSv4.2
Draft 2016
Server Side Copy
Application Input/Output (I/O) Advise
Sparse Files hole punching and Space Reservations
Application Data Block (ADB) Support
Labeled NFS
[Speaker Notes: https://tools.ietf.org/html/draft-ietf-nfsv4-minorversion2-41 Application Input/Output (I/O) Advise - allows servers to optimize future I/O requests for a file by for example, prefetching or evicting data (may be helpful to applications such as databases and video editors) Sparse files are ones which have unallocated or uninitialized data blocks as holes in the file. Such holes are typically transferred as 0s when read from the file. READ_PLUS allows a server to send back to the client metadata describing the hole and DEALLOCATE allows the client to punch holes into a file (a portion of the file can be marked as unwanted and the associated storage released). In addition, SEEK is provided to scan for the next hole or data from a given location Space Reservations When a file is sparse, one concern applications have is ensuring that there will always be enough data blocks available for the file during future writes. ALLOCATE allows a client to request a guarantee that space will be available. Also DEALLOCATE allows the client to punch a hole into a file, thus releasing a space reservation. Application Data Block (ADB) Support - Some applications treat a file as if it were a disk and as such want to initialize (or format) the file image. The WRITE_SAME is introduced to send this metadata to the server to allow it to write the block contents. Labeled NFS is an effort to provide the mechanisms required to use Mandatory Access Control systems with NFSv4 (the ability to enforce ACL on top of users’ ACLs;)]

---
Thank you